Repair defective backlite Motu 828 MKII

Based on forum topic “MOTU 828 mkII USB crackle”, I tried to replace the backlite LED, as described by LeeYoo’s post topic #17.

http://www.gearslutz.com/board/so-much-gear-so-little-time/449416-motu-828-mkii-usb-crackle.html

1. Dismounting

Dismount Main Board: Screws are indicated in red.

Difficult dismounting area.

Bottom plate:

Dismounted boards:

Screw with plastic isolation washer. It should be placed on the same position as original since it need to avoid short circuit if bare screw head touches traces on the board.

Front side LCD display

Dismount defective LED assembly by breaking it out by wringing on the solder wires

Prepare new High Brightness LED

Solder new LED on solder pad’s old LED assembly

If foil is bended, you can keep it on it’s place by double sided tape

This is the result:

# Text boxes

Earth connection IEC320

Transformer  mounting screws

PCB mounting screws

Front knobs

Desolder SMD LED assembly

Anode – Positive voltage – smalest part in LED

Kathode – Negative voltage – biggest part in LED

Take care LED wires not making contact with IC’s pens